## Slide 1: E3D Processes on Behavioral Data
Lucie Huet
November 10, 2014

## Slide 2: Workflow Overview
Tracking: Track Whisker in 2 camera views
Pre-processing: Obtain two smooth 2D whiskers, C, CP, BP (make sure X-Y is top-down and X-Z front-on)
3D merging: Obtain one smooth 3D whisker, 3D-CP,BP (C should remain the same)
E3D Wrapper: Calculate TH, PHI, PHI_euler, whisker zeta (both tracked and estimated), and select reference whiskers
Questions to think about: what gets filtered when?
Neural/tracking people do this
E3D wrapper people do this

## Slide 3: Organization is key!!!
Because this project traverses multiple people and we hope to put large amounts of data through this flow, it is extremely important we keep consistent code and data formatting.
Two major things to keep track of:
The code used
  Updates are important!
  Currently, most code is in Dropbox folder VG_Sync
    Best practice would be to work off this folder in MATLAB instead of downloading.
  In the (near) future: move to a GitHub account
    Will require manual updating, but relatively easy to do, also does version control.
The files that store all the data
  Naming convention is important!

## Slide 4: Current/historical Data Format:
Preprocessing uses code:
VG_Sync/Track_VG_Featers/Run_Process_2D_WSKR_v3
  (Used to be part of VG_Sync/Track_VG_Features/VG2D_RUN_ALL_V4)
Unfortunately, I don't know much else about what goes on here anymore, and the process is subject to change.
THE FUTURE:
  in Run_Process_2D_WSKER_v3, it calls the function process_TH_BP_v5.m (or a name similar to that). This process of calculating TH and PHI (once in top-down for TH and once in front-on view for PHI (projection)) will incorporated into E3D wrapper. BP calculation is likely to stay with neural/tracking people.

## Slide 5: .mat files for E3D wrapper
E3D wrapper is handed 2 .mat files:
Vg_DAT_3D_Merge_[data tag].mat
  xw3d – n x 1 cell array, each cell contains the x-coordinates for the whisker in one frame
  yw3d – n x 1 cell array, y-coordinates
  zw3d – n x 1 cell array, z-coordinates
    1st element of array per cell is base node of whisker
    unit is pixels
Vg_DATA_3D_TH_PHI_C_CP_BP_[data tag].mat
  C – n x 1 logical array with 0 for non-contact frames and 1 for contact frames
  CP – n x 3 array giving contact point locations, fill in non-contact frames with NaNs
  TH – n x 1 array giving theta angle of whisker in world coordinates (used to be TH_world, now is just TH)
  PHI – n x 1 array giving projection phi angle in world coordinates
  BP – n x 3 array giving basepoint location
THE FUTURE: TH and PHI will be calculated by E3D wrapper

## Slide 6: The Settings File
The best way (so far) to hold parameters for each trial
.m file that creates a struct, PT, that holds parameters to be used throughout the code
Currently, there's one settings file for preprocessing and one for the E3D wrapper, but for THE FUTURE, they really should get combined
  Settings_VG3D_[data tag].m/ Settings_VG2D_[data tag].mat
Settings file contents:
  Comments at the top give basic information, who took this data and when, awake or anesthetized, etc.
  PT. (list on next slide)

## Slide 7: Settings File part 2:
PT. (perhaps complete list)
  data – path name to where the .mat data files are stored – unique per computer
  save – path name for where you want the output of the data will be saved (often same as PT.data)
  Frames – 1 x 2 array showing start and end frames used, e.g. [101 2100]
  TAG – the tag to be used when marking data, usually the date (e.g. 20141023), then some short information (e.g. T07 for trial 7), and then the frames formatted as (F0101F2100).
  pix2m – pixels to meters conversion (how many meters to a pixel – a very small number)
  proc_base_segment – 1 x 2 array saying how much of the whisker (the linear portion at the base) to consider when calculating TH and PHI (first # is non-zero so possibly noisy basepoint is excluded, second # generally around 4 mm) – in mm
  REF – denote, if desired, which frames to use as reference frames
  pct_planer – what percentage of the whisker arclength should be considered planar for zeta calculation (typically 0.7)
  E3D_E – Young's modulus (typically 3.3 GPa)
  E3D_rbase – base radius (typically 100e-6)
  E3D_taper – base to tip ratio (typically 15)
  filt – filter coefficient, calculated as (desired cutoff Hz/(sampling Hz/2) ), though maybe filtering will be applied earlier
tracking provides these three
used in E3D wrapper, probably added by E3D wrapper people
File storage stuff changes per computer

## Slide 8: E3D Wrapper output
Vg_DATA_3D_PROC_[data tag].mat
  PHIE – euler PHI
  x/y/zw3dm – same as x/y/zw3d, but in meters
  BPm, CPm – same as BP, CP but in meters
  S_max – of all timeframes, the maximum whisker arclength, which will be set to the "actual" whisker arclength
  ZETA – zeta angle of whisker (as measured)
  ZETA_NC – zeta angle as predicted using non-contact frames and theta
  REF – n x 1 array saying which time frame was used as a reference whisker for every frame of contact (soon to be obsolete)
THE FUTURE
  TH – theta angle
  PHI – projection phi (calculated before PHIE)

## Slide 9: E3D Output
VG_E3D_[data tag].mat
  BPm_filt, CPm_filt, ZETA_NC_filt, TH_filt, PHIE_filt, ZETA_filt – filtered versions of each of these variables, perhaps not all will be kept, depending on how tracking works out.
  F – n x 3 array giving [Fx, Fy, Fz] for every frame of contact – whisker coordinates
  M – n x 3 array giving [Mx, My, Mz] for every frame of contact – whisker coordinates
  S_app, F_app, Z_app – optimization solutions for E3D: the arc length along the whisker at which the force was applied, the magnitude of the force applied, and the angle about the whisker's axis that the force was applied.
  x/y/ze3d – x,y,z, coordinates of deflected whisker from E3D in meters and world coordinates
  POS – n x 3 array saying the final contact point output in E3D – potentially different from CPm_filt
  Err_all – n x 1 cell array giving the error for every node along the whisker arc length for each frame
  Err_max – n x 1 array giving maximum error across arc length for every frame
  Err_mean – n x 1 array giving mean error across arc length for every frame
  Err_cp – I forget, either the Euclidean distance between CPm_filt and POS or the error

## Slide 10: Data Quality
No NaN gaps in x/y/zw3d, TH, PHI, C, CP, or BP
Whiskers must be smooth and sufficiently long (preferably extend 15% past contact point)
Whisker must have sufficient number of nodes – preferably around 100, at least 40 is best.
BIG QUESTION: What to filter when?
  Currently, almost everything gets filtered in the E3D wrapper, but that may change.
  BP may get filtered by the neural people but should always be filtered before running E3D
  TH, PHIE, CP might not need to be filtered before running E3D (and, by extension, ZETA_NC)

## Slide 11: Code/data storage cleanup is necessary
Just a reminder to keep things organized! The code is currently under development as improvements to tracking are made and TH and PHI are handed over to E3D wrapper to calculate.
So, make sure data tags are neat and unique (one Settings file per trial/run through of data).